## Slide 1: TEST SYSTEM DEVELOPMENT FOR RADIATION EFFECTS ON EDAC
PRESENTED BY-
AAKRITI AGRAWAL-2015A3PS276P
A LOHITH -2015A3PS215H
MENTORS-
Mr. PARVEEN RANA
Mr. S.N. MITTAL
SEMICONDUCTOR LABORATORY – VLSI TESTING DIVISION
SUBMITTED TO-
Dr. RAJEEV TALIYAN

## Slide 2: INTRODUCTION
The Digital world is of only 0s and 1s
A : 1010 :some event: 1110 : E
Spacecraft Cassini–Huygens, launched in 1997, contains two identical flight recorders, each with 2.5 gigabits of memory in the form of arrays of commercial DRAM chips.
Thanks to built-in EDAC functionality!
(the spacecraft reported a nearly constant single-bit error rate of about 280 errors per day)
ECC Memory – Error Correcting Code Memory

## Slide 3: HAMMING CODE
HISTORY
Richard Hamming 1950
American mathematician
BELL LABS
WHAT IS PARITY?
Check bit
Simplest form of error detecting code

## Slide 4: Let’s implement what we have just learnt
01011001
_ _ 0 _ 1 0 1 _ 1 0 0 1 _
P0: XOR(0,1,1,1,0)=1
P1: XOR(0,0,1,0,0)=1
P2: XOR(1,0,1,1)=1
P3: XOR(1,0,0,1)=0
P4: XOR(1,0,0,1,1,0,1,0,1,1,1,0)=1
Lets introduce Error at Position D5
01011101
_ _ 0 _ 1 0 1 _ 1 1 0 1 _
P0: XOR(0,1,1,1,0)=1
P1: XOR(0,0,1,1,0)=0
P2: XOR(1,0,1,1)=1
P3: XOR(1,1,0,1)=1
P4: XOR(0,1,0,1,1,1,0,1,1,0,1,1)=0
2+8=10 => Bit Error at Position 10.

## Slide 5: EDAC
CONTROL SIGNALS FOR -
READING DATA
WRITING DATA
1 MHz

## Slide 6: TEST SYSTEM DESIGN
PIC
- Used to control EDAC.
- Send Control Signals to EDAC.
- Sends Data and Address via port.
- Reads output via port.
- Communicates output
via USART.

## Slide 7: FLOWCHART
WRITE CYCLE AT FRONTEND

## Slide 8
WRITE CYCLE AT BACKEND
Write control signals to EDAC

## Slide 9
READ CYCLE
AT FRONTEND

## Slide 10
READ CYCLE
AT BACKEND
Read control signals to EDAC

## Slide 11: SERIAL COMMUNICATION
END ADD
@
START ADD
#
START ADD
PARITY
END ADD
DATA
END ADD
$
START ADD
#
START ADD
HAMMOUT
END ADD
SYNDROME
NO ERROR
1 BIT ERROR
2 BIT ERROR
Asynchronous serial communication.
USART protocol is used.
Current baud rate is 9600.
8 bits preceded by start bit and succeeded by stop bit is transferred at a time.
PC
PIC
WRITE CYCLE FORMAT
READ CYCLE FORMAT

## Slide 12
POWER SUPPLY
EDAC
PIC
MAX 232
Brings voltage levels of PIC and PC within desired limit to carry out communication between them.
SCHEMATIC

## Slide 13: Graphical User Interface

## Slide 14: DEMONSTRATION

## Slide 15: FURTHER WORK
Increasing Internal clock frequency and Baud Rate.
Maintain a Data Log along with Summary of the test values.
Automate the entire process with a single button for SEE Testing.

## Slide 16: Any Questions/Doubts and Suggestions are most welcomed